Issued Date:  		Wednesday, April 17, 2024

District:	 	Yuba Community College District

3301 E Onstott Rd

Yuba City, CA 95991

Contact: David Willis, Dir. Facilities Planning, Maintenance & Operations

Job Location:	Yuba Community College

2088 N Beale Rd

Marysville, CA 95901

Architect:		Hibser Yamauchi Architects, Inc.

4602 2nd St

Davis, CA 95618

This Addendum has been prepared to clarify, modify, delete, or add to the drawings and/or specifications for the above referenced project, and revisions to items listed here shall supersede description thereof prior to the above stated date.  All conditions not specifically referenced here shall remain the same.  It is the obligation of the Prime Contractor to make subcontractors aware of any items herein that may affect submitted bids. Acknowledge receipt of this addendum by inserting its number and date in the bidding documents.  Failure to do so may subject bidder to disqualification. All addenda items refer to the plans and specifications unless specifically noted otherwise.

PART A – GENERAL

None.

PART B – BIDDING AND CONTRACT REQUIREMENTS

Refer to PART E for related RFI responses.

## PART C – CHANGES/CLARIFICATIONS TO TECHNICAL SPECIFICATIONS

  - SECTION 09 51 53 – ADHESIVE APPLIED ACOUSTICAL CEILINGS.

- ADD Section 09 51 53 in its entirety.  See attached.

PART D – CHANGES/CLARIFICATIONS TO DRAWINGS:

None.

PART E – RFI RESPONSES:

- Room 200 has acoustic spray on popcorn on the walls behind stage curtain and side walls is this being removed?

Existing textured wall finish to remain. Provide wall paint finish as indicated per GENERAL FINISH NOTES no. 4 on Sheet I2.00.

- Room 200 glue ceiling tiles is suppose to be removed. What is going back in that location?

Existing glue-up ceiling tiles to remain in room.  Paint existing finish as indicated per Item No.1.11.D.3 of Addendum No.1.

- Room 201 is all wood walls Just confirming we are just painting this and not overlaying with drywall there is no mention of drywall?

Remove all floor-to-ceiling existing 1/4" wood paneling throughout LECTURE HALL 201 room (on all four walls).  Provide new 1/4" gypsum board finish over  existing 5/8” gypsum board substrate OR provide new 5/8” gypsum board wall finish over existing framing. Texture and paint to achieve smooth and uniform finish.

- Rooms 211 210 209 208 206 205 204 203 has glue on ceiling tiles. Reflected ceiling plans says Acoustical tile on existing grid. What are we doing here [?] new glue on tiles [?]  The demo has the glue on tiles on walls being removed but [does not] mention on ceiling? Are we installing new grid and tile?

Remove existing glue-up ceiling tiles in these rooms and coordinate with all overhead work. Also provide the following:

  - New replacement glue-up tiles in PRACTICE 206 thru 210 rooms.  Patch and repair of existing gypsum substrate OR provide new 5/8" gypsum substrate over existing framing to receive tiles.  Refer to attached Section 09 51 53.

  - New 1/4" gypsum board over existing gyp board substrate OR provide new 5/8” gypsum over existing framing to establish smooth uniform finish in COMPUTER LAB 203 and OFFICE 204, 205, and 211 rooms.

- In building 1000 there is a classroom that has theatrical lighting installed on the ceiling. (a) is it going to be removed or remain? If it remains who is responsible to take down and reinstall?

Contractor to replace suspended acoustical ceiling tiles with existing theatrical lighting protected and in place.  Contractor may cut/modify new tiles to fit around lighting supports if necessary.  Provide infill trim to minimize any visible gaps.

- There are no Fire Alarm devices shown. The drawing says: may need to be removed and replaced in same location. Please provide existing locations and the addresses of each device, to be removed and replaced.

Existing fire alarm devices shall remain and be protected during construction.

- What Fire Alarm system manufacturer is installed?

Edwards EST is the existing fire alarm system.

- Is there a path in place at building 1000 for Data cabling across breeze ways between building segments?

Existing path exists and allow existing cabling to IDF.  Contractor to re-use existing path or establish new path(s) within connecting exterior soffits between buildings.

- The Hazardous Material Survey lab results shown for Bldg 200, No asbestos material & for Bldg 1000, No asbestos material. However, according to Addendum 1 Part D, 1.6, D. Clarification Item 1) Room 201 Lecture Hall, has “Existing VCT is known to be asbestos containing.

Assume all 9x9 VCT and mastic under tiles to be asbestos containing.

- While at the job walk, it was noticed that suspect 9” floor tile was under the carpet in other locations.  It is difficult to determine exactly which floors may have the asbestos tile. Please advise.

Provide new carpeting over existing 9x9 VCT throughout PRACTICE 200 and 202 rooms.

- Bldg. 200 -The Drinking Fountain is to be relocated by the women’s side but there is a hose bibb (picture attached). Is that hose bibb staying on place or being relocated with the drinking fountain?

Existing hose bib to remain.

- Bldg. 1000 -In Room 1005 there is an existing 2 comp sink or you wanting it replaced with a 3-comp sink or a 2-comp?

Existing sink(s) in CERAMIC STUDIO 1005 room to remain. Contractor to clean existing sink (s) and faucets.

- Bldg. 1000 -In Room 1001 (Please see attached plan sheets). On the demo Plumbing sheet, it is calling out to demo the sink & salvage. Are we salvaging the faucet & eyewash? It is not clear what we are salvaging.

Disconnect and temporarily remove existing sink and faucet as needed to replace PLAM finish at existing counters.  Contractor to clean and re-install existing sink, faucet and eyewash.

- Will a non-collusion form be provided for the bid package?

Please refer to the attachment Section 00 45 19 Non-Collusion Affidavit.

- Will a site certification form be provided, or shall we use the sign in sheet?

There is not a Certification Form required on this project.

- Per Section 00 41 00 Bid form Page 1 of 6, 1. Introduction, E. The signed copy of the certification of the visit to the site shall be attached to the Bid form submittal. What certification form is this?

There is not a Certification Form required on this project. The District has posted the Mandatory Pre-Bid Sign-In Log Sheet.  Only Contractors that have attended and signed the Mandatory Pre-Bid Sign-In Log Sheet are allowed to bid this project.

- Per Appendix B- Insurance:

  - Item 1. We have a $5,000 deductible; will you accept this?

Yes.  The deductible is required to be paid 100% by the contractor.

  - Item 5. Builders Risk- If applicable- does this apply to this project?

Yes.  The deductible is required to be paid 100% by the contractor. The Contractor is fully responsible to both open and secure the buildings at the start and end of the contractors work shifts and to also secure all construction materials and equipment in secure lockable temporary containers provided by the contractor. Include other requirements that apply to the Builders Risk insurance per sections 5 through 9.

List of Attachments

- Section 09 51 53 – Adhesive Applied Acoustical Ceilings

- Section 00 45 19 Non-Collusion Affidavit

End of Addendum No.3